## Slide 1
Unit III: Control Unit Organization
Hardwired Control Unit and Timing Signals,
Microprogrammed control unit:
  control memory,
  Address sequencing,
  Microprogram Example, Designing of microprogrammed control unit.
  Comparison of hardwired and microprogrammed control units,
    RISC and CISC Processors

## Slide 2: Control Unit
Present in CPU
Coordinate between CPU , Main memory, I/O devices
Types
  Hardwired Control unit
    Made hardware components like logic gates, flip flops, decoders, registers etc.
  Microprogrammed Control Unit
    Designed using microprogram, controlled memory

## Slide 3: Hardwired Control unit
Uses fixed logic circuits to generate control signals
Faster than microprogrammed control units
Difficult to modify or update once designed
Typically found in RISC processors
Efficient for simple, high-speed operations

## Slide 4: Hardwired Control unit
Advantages:
Faster execution due to dedicated circuits
Less memory usage compared to microprogrammed units
Immediate response without delay from memory access
Disadvantages:
Difficult to modify or upgrade
Complex logic design for modern instruction sets
Less flexible compared to microprogrammed control

## Slide 5: Hardwired Control unit
Working Principle
  Input: Opcode from instruction register
  Control logic generates necessary control signals
  Uses combinational circuits (AND, OR, NOT gates)
  Generates precise signals for ALU, registers, memory, and buses
  Works in synchronization with system clock

## Slide 6: Hardwired Control unit
Decoder input 3 bit
Decoder output 8 bit
E.g. 000,001,010, ..

## Slide 7: Hardwired Control unit
Timing Signals
  Signals that synchronize operations within a CPU
  Generated by system clock or control unit
  Ensure correct sequence of instruction execution
  Used to control data transfer between registers and memory
  Essential for synchronous digital circuits
Working Methods
  System clock generates periodic pulses
  Control unit decodes instructions & generates timing signals
  Each instruction phase (fetch, decode, execute) gets a timing signal
  Ensures proper data flow across CPU components
  Prevents race conditions and timing mismatches

## Slide 8: Hardwired Control unit
Example: Executing ADD R1, R2, R3
T1: Fetch instruction from memory
T2: Decode instruction in control unit
T3: Read operands R2, R3 from register file
T4: Perform addition in ALU
T5: Store result in R1 Each step is activated by a specific timing signal

## Slide 9: Microprogrammed Control Unit
Uses a control memory to store microinstructions
Executes microinstructions sequentially
Flexible and easier to modify than hardwired control
Common in CISC architectures
Slower than hardwired control due to memory access

## Slide 10: Control Memory
Stores microinstructions for control signals
ROM or writable memory used for microprogram storage
Fetch-decode-execute cycle guided by microinstructions
Each microinstruction specifies control signals
Example: Fetch instruction from memory, decode opcode, execute

## Slide 11: Address Sequencing
Determines next microinstruction to execute
Types of sequencing:
  Incrementing control memory address
  Branching based on condition flags
  Indirect address from control memory
Optimizes execution path in control unit
Example: Conditional branching in microprogram execution

## Slide 12: Microprogram Example
Example: Execution of ADD R1, R2
  Step 1: Fetch instruction from memory
    MAR ← PC, Read Memory
    PC ← PC + 1, IR ← MDR
  Step 2: Decode instruction Identify opcode and source/destination registers
  Step 3: Execute ADD operation
    R1 ← R1 + R2

## Slide 13: Comparison
Hardwired Control Unit:
Uses fixed logic circuits for control signals
Faster execution due to direct hardware implementation
Difficult to modify or update
Common in high-performance processors
Microprogrammed Control Unit:
Uses a control memory storing microinstructions
Easier to modify and implement complex instructions
Slower due to memory access overhead
Common in CISC architectures

## Slide 14: Essential Instructions for the Processor
Load (LD) / Store (ST) - Transfer data between memory and registers
Add (ADD) / Subtract (SUB) - Perform basic arithmetic operations
AND, OR, XOR, NOT - Logical operations for decision making
Jump (JMP) / Conditional Jump (JMPZ, JMPL) - Control flow management
Shift Left (SHL) / Shift Right (SHR) - Bitwise operations for efficiency

## Slide 15: Sample Assembly Code Execution
Example: Computing C = A + B and storing in memory
  LD R1, A ; Load A into register R1
  LD R2, B ; Load B into register R2
  ADD R3, R1, R2 ; R3 = R1 + R2
  ST R3, C ; Store result in memory

## Slide 16: MICROPROGRAMMED CONTROL Control Memory
Microprogram
- Program stored in memory that generates all the control signals required to execute the instruction set correctly
- Consists of microinstructions
- It is generally ROM.
Microinstruction
- Contains a control word and a sequencing word
Control Word - All the control information required for one clock cycle
Sequencing Word - Information needed to decide the next microinstruction address
- Vocabulary to write a microprogram
Control Memory(Control Storage: CS)
- Storage in the microprogrammed control unit to store the microprogram
Writeable Control Memory(Writeable Control Storage: WCS)
- CS whose contents can be modified
-> Allows the microprogram can be changed
-> Instruction set can be changed or modified

## Slide 17
Dynamic Microprogramming
- Computer system whose control unit is implemented with
a microprogram in WCS
- Microprogram can be changed by a systems programmer or a user
Fig: Microprogrammed Control Organization
Sequencer (Microprogram Sequencer)
A Microprogram Control Unit that determines the Microinstruction Address to be executed in the next clock cycle
- In-line Sequencing
- Branch
- Conditional Branch
- Subroutine
- Loop
- Instruction OP-code mapping
Control
word
Next Address
Generator
(sequencer)
CAR
Control
Memory
(ROM)
CDR
External
input
CAR- Control Address Register
CDR- Control Data Register

## Slide 18: ADDRESS SEQUENCING (Microprogram )
Sequencing Capabilities Required in a Control Storage
- Incrementing of the control address register
- Unconditional and conditional branches
- A mapping process from the bits of the machine instruction to an address for control memory
- A facility for subroutine call and return
Instruction code
Mapping
logic
Multiplexers
Control memory (ROM)
Subroutine
register
(SBR)
Branch
logic
Status
bits
Microoperations
Control address register
(CAR)
Incrementer
MUX
select
select a status
bit
Branch address
-microprogram contents micro instructions
-microinstruction contents micro-operations
Control memory stores micro program

## Slide 19: ADDRESS SEQUENCING (Microprogram )
Process
  Increment CAR by 1
  Subroutine Register (Collection of instruction) : for repetitions of instruction like recursive functions
  conditional and unconditional branch
    Conditional: check the condition. Then load the address in CAR. Check the status bit then load accordingly
    Unconditional: without checking the condition the corresponding register address will be loaded into CAR
  Mapping Instruction: Mapping logic (Next slide)
Instruction code
Mapping
logic
Multiplexers
Control memory (ROM)
Subroutine
register
(SBR)
Branch
logic
Status
bits
Microoperations
Control address register
(CAR)
Incrementer
MUX
select
select a status
bit
Branch address

## Slide 20: MAPPING OF INSTRUCTIONS
ADD Routine
AND Routine
LDA Routine
STA Routine
BUN Routine
Control
Storage
0000
0001
0010
0011
0100
OP-codes of Instructions
ADD
AND
LDA
STA
BUN
0000
0001
0010
0011
0100
.
.
.
Direct Mapping
Address
10 0000 010
10 0001 010
10 0010 010
10 0011 010
10 0100 010
Mapping
Bits
10 xxxx 010
ADD Routine
Address
AND Routine
LDA Routine
STA Routine
BUN Routine
LDA : Load Accumulator
STA : Store Accumulator
BUN: Branch Unconditionally

## Slide 21: MAPPING OF INSTRUCTIONS TO MICROROUTINES
Mapping function implemented by ROM or PLA
Mapping from the OP-code of an instruction to the
address of the Microinstruction which is the starting
microinstruction of its execution microprogram
1 0 1 1 Address
OP-code
Mapping bits
Microinstruction
address
0 x x x x 0 0
0 1 0 1 1 0 0
Machine
Instruction
OP-code
Mapping memory
(ROM or PLA)
Control address register
Control Memory
PLA: Programmable Logic Array

## Slide 22: MICROPROGRAM EXAMPLE
Computer Configuration
MUX
AR
10
0
PC
10
0
Address
Memory
2048 x 16
MUX
DR
15
0
Arithmetic
logic and
shift unit
AC
15
0
SBR
6
0
CAR
6
0
Control memory
128 x 20
Control unit

## Slide 23: MACHINE INSTRUCTION FORMAT
Microinstruction Format
EA is the effective address
Symbol OP-code Description
  ADD 0000 AC AC + M[EA]
  BRANCH 0001 if (AC < 0) then (PC  EA)
  STORE 0010 M[EA]  AC
  EXCHANGE 0011 AC  M[EA], M[EA]  AC
Machine instruction format
Sample machine instructions
F1
F2
F3
CD
BR
AD
3
3
3
2
2
7
F1, F2, F3: Microoperation fields
CD: Condition for branching
BR: Branch field
AD: Address field
I
Opcode
15
14
11
10
Address
0

## Slide 24: MICROINSTRUCTION FIELD DESCRIPTIONS - F1,F2,F3
F1 Microoperation Symbol
000 None NOP
001 AC  AC + DR ADD
010 AC  0 CLRAC
011 AC  AC + 1 INCAC
100 AC  DR DRTAC
101 AR  DR(0-10) DRTAR
110 AR  PC PCTAR
111 M[AR]  DR WRITE
F2 Microoperation Symbol
000 None NOP
001 AC  AC - DR SUB
010 AC  AC  DR OR
011 AC  AC  DR AND
100 DR  M[AR] READ
101 DR  AC ACTDR
110 DR  DR + 1 INCDR
111 DR(0-10)  PC PCTDR
F3 Microoperation Symbol
000 None NOP
001 AC  AC  DR XOR
010 AC  AC’ COM
011 AC  shl AC SHL
100 AC  shr AC SHR
101 PC  PC + 1 INCPC
110 PC  AR ARTPC
111 Reserved

## Slide 25: MICROINSTRUCTION FIELD DESCRIPTIONS - CD, BR
CD Condition Symbol Comments
00 Always = 1 U Unconditional branch
01 DR(15) I Indirect address bit
10 AC(15) S Sign bit of AC
11 AC = 0 Z Zero value in AC
  BR Symbol Function
  00 JMP CAR  AD if condition = 1
  CAR  CAR + 1 if condition = 0
  01 CALL CAR  AD, SBR  CAR + 1 if condition = 1
  CAR  CAR + 1 if condition = 0
  10 RET CAR  SBR (Return from subroutine)
  11 MAP CAR(2-5)  DR(11-14), CAR(0,1,6)  0

## Slide 26: SYMBOLIC MICROINSTRUCTIONS
Symbols are used in microinstructions as in assembly language
A symbolic microprogram can be translated into its binary equivalent by a microprogram assembler.
Sample Format
five fields: label; micro-ops; CD; BR; AD
  Label: may be empty or may specify a symbolic address terminated with a colon
  Micro-ops: consists of one, two, or three symbols
  separated by commas
  CD: one of {U, I, S, Z}, where U: Unconditional Branch
  I: Indirect address bit
  S: Sign of AC
  Z: Zero value in AC
  BR: one of {JMP, CALL, RET, MAP}
  AD: one of {Symbolic address, NEXT, empty}

## Slide 27: SYMBOLIC MICROPROGRAM - FETCH ROUTINE
Symbolic microprogram for the fetch cycle:
Binary equivalents translated by an assembler
1000000 110 000 000 00 00 1000001
1000001 000 100 101 00 00 1000010
1000010 101 000 000 00 11 0000000
Binary
address F1 F2 F3 CD BR AD
During FETCH, Read an instruction from memory
and decode the instruction and update PC
AR PC
DR  M[AR], PC  PC + 1
AR  DR(0-10), CAR(2-5)  DR(11-14), CAR(0,1,6)  0
ORG 64
PCTAR U JMP NEXT
READ, INCPC U JMP NEXT
DRTAR U MAP
FETCH:
Sequence of microoperations in the fetch cycle:

## Slide 28: SYMBOLIC MICROPROGRAM
Control Storage: 128 20-bit words
The first 64 words: Routines for the 16 machine instructions
The last 64 words: Used for other purpose (e.g., fetch routine and other subroutines)
Mapping: OP-code XXXX into 0XXXX00, the first address for the 16 routines are
0(0 0000 00), 4(0 0001 00), 8, 12, 16, 20, ..., 60
Partial Symbolic Microprogram
ORG 0
NOP
READ
ADD
ORG 4
NOP
NOP
NOP
ARTPC
ORG 8
NOP
ACTDR
WRITE
ORG 12
NOP
READ
ACTDR, DRTAC
WRITE
ORG 64
PCTAR
READ, INCPC
DRTAR
READ
DRTAR
I
U
U
S
U
I
U
I
U
U
I
U
U
U
U
U
U
U
U
CALL
JMP
JMP
JMP
JMP
CALL
JMP
CALL
JMP
JMP
CALL
JMP
JMP
JMP
JMP
JMP
MAP
JMP
RET
INDRCT
NEXT
FETCH
OVER
FETCH
INDRCT
FETCH
INDRCT
NEXT
FETCH
INDRCT
NEXT
NEXT
FETCH
NEXT
NEXT
NEXT
ADD:
BRANCH:
OVER:
STORE:
EXCHANGE:
FETCH:
INDRCT:
Label Microops CD BR AD

## Slide 29: BINARY MICROPROGRAM
This microprogram can be implemented using ROM
  Address Binary Microinstruction
  Micro Routine Decimal Binary F1 F2 F3 CD BR AD
ADD 0 0000000 000 000 000 01 01 1000011
  1 0000001 000 100 000 00 00 0000010
  2 0000010 001 000 000 00 00 1000000
  3 0000011 000 000 000 00 00 1000000
BRANCH 4 0000100 000 000 000 10 00 0000110
  5 0000101 000 000 000 00 00 1000000
  6 0000110 000 000 000 01 01 1000011
  7 0000111 000 000 110 00 00 1000000
STORE 8 0001000 000 000 000 01 01 1000011
  9 0001001 000 101 000 00 00 0001010
  10 0001010 111 000 000 00 00 1000000
  11 0001011 000 000 000 00 00 1000000
EXCHANGE 12 0001100 000 000 000 01 01 1000011
  13 0001101 001 000 000 00 00 0001110
  14 0001110 100 101 000 00 00 0001111
  15 0001111 111 000 000 00 00 1000000
FETCH 64 1000000 110 000 000 00 00 1000001
  65 1000001 000 100 101 00 00 1000010
  66 1000010 101 000 000 00 11 0000000
INDRCT 67 1000011 000 100 000 00 00 1000100
  68 1000100 101 000 000 00 10 0000000

## Slide 30: DESIGN OF CONTROL UNIT - DECODING ALU CONTROL INFORMATION -
microoperation fields
3 x 8 decoder
7
6
5
4
3
2
1
0
F1
3 x 8 decoder
7
6
5
4
3
2
1
0
F2
3 x 8 decoder
7
6
5
4
3
2
1
0
F3
Arithmetic
logic and
shift unit
AND
ADD
DRTAC
AC
Load
From
PC
From
DR(0-10)
Select
0
1
Multiplexers
AR
Load
Clock
AC
DR
DRTAR
PCTAR

## Slide 31: MICROPROGRAM SEQUENCER - NEXT MICROINSTRUCTION ADDRESS LOGIC -
MUX-1 selects an address from one of four sources and routes it into a CAR
- In-Line Sequencing  CAR + 1
- Branch, Subroutine Call  CS(AD)
- Return from Subroutine  Output of SBR
- New Machine instruction  MAP
Branch, CALL Address
Subroutine
CALL
3
2
1
0
S
S
1
0
MUX1
External
(MAP)
SBR
L
Incrementer
CAR
Clock
Address
source
selection
In-Line
RETURN form Subroutine
Control Storage
S1S0 Address Source
00 CAR + 1, In-Line
01 SBR RETURN
10 CS(AD), Branch or CALL
11 MAP

## Slide 32: MICROPROGRAM SEQUENCER - CONDITION AND BRANCH CONTROL -
Input
logic
I0
I1
T
MUX2
Select
1
I
S
Z
Test
CD Field of CS
From
CPU
BR field
of CS
L(load SBR with PC) for subroutine Call
S0
S1
for next address
selection
I0I1T Meaning Source of Address S1S0 L
000 In-Line CAR+1 00 0
001 JMP CS(AD) 01 0
010 In-Line CAR+1 00 0
011 CALL CS(AD) and SBR <- CAR+1 01 1
10x RET SBR 10 0
11x MAP DR(11-14) 11 0
L
S0 = I0
S1 = I0I1 + I0’T
L = I0’I1T
Input Logic

## Slide 33: MICROPROGRAM PROGRAMMED CONTROL
3
2
1
0
S1
MUX1
External
(MAP)
SBR
Load
Incrementer
CAR
Input
logic
I1
0
T
MUX2
Select
1
I
S
Z
Test
Clock
Control memory
Microops
CD
BR
AD
L
I
S0
. . .
. . .

## Slide 34: MICROINSTRUCTION FORMAT
Information in a Microinstruction
- Control Information
- Sequencing Information
- Constant
Information which is useful when feeding into the system
These information needs to be organized in some way for
- Efficient use of the microinstruction bits
- Fast decoding
Field Encoding
- Encoding the microinstruction bits
- Encoding slows down the execution speed
due to the decoding delay
- Encoding also reduces the flexibility due to
the decoding hardware